## Slide 1: DESIGN & ANALYSIS OF SWIMMING POOL LIFT
Group Members:
1. ED15B001 ADARSH S.
2. ME15B044 AKSHAY M.
3. ME15B048 NIKHIL S.
4. ME15B079 ABHIJEET V.
ME6221: THEORY OF MECHANISMS
PROF. SUJATHA SRINIVASAN

## Slide 2: OBJECTIVES
Design a swimming pool lift for a wheelchair user in accordance with American with Disability Act 2010
Perform four position motion synthesis to develop a four bar mechanism
Balance the mechanism against toppling
Propose a driver dyad for actuation with high mechanical advantage with optimal link lengths for least force of actuation
Incorporate spring balancing into the design to minimize torque requirements

## Slide 3: METHODOLOGY
4 Position Synthesis
Counterbalancing
Driver Dyad Synthesis
Force Analysis
Spring balancing

## Slide 4: SITE SURVEY
Criteria:
  Wheelchair accessibility
  Depth of the pool
  Space availability for accommodating mechanism

## Slide 5: KINEMATIC SYNTHESIS
Initial & final positions chosen based on ADA requirements
  (x0,y0) = (-405 mm,485 mm)
  (xf,yf) = (700mm,-455mm)

## Slide 6: KINEMATIC SYNTHESIS
3 Position synthesis was initially performed to find approximate location of fixed pivots

## Slide 7: KINEMATIC SYNTHESIS
4 position synthesis performed afterward to generate best locations for fixed pivots

## Slide 8: KINEMATIC SYNTHESIS
Link | Length(m) | Direction(deg) at initial pose
Crank length l1 | 0.941 | 179.18
Dyad 1 length l2 | 1.976 | -54.73
Follower length l3 | 1.235 | -166.32
Dyad 2 length l4 | 1.351 | -42.21
Coupler length l5 | 0.719 | -78.77
Base length l6 | 0.565 | -45.00

## Slide 9: COUNTERBALANCING
2 extreme scenarios:
  The person is seated & the mechanism is at its extreme position into the water
  There is no one sitting on the mechanism & the mechanism is at its initial position
If we are counterbalancing purely by a mass, then required mass = 150 kgs

## Slide 10: COUNTERBALANCING
Alternate proposal: Attach buoys to the frame/mechanism through rigid links
Buoys can be lowered into the water only when necessary & then removed
With a counterbalance of 20 kgs, the buoys need to displace a volume of water equal to around 65 litres at a distance 1.5 m into the pool to provide sufficient counter-moment
As we have control over how the buoys are lowered into the pool, we can ensure the system doesn’t topple in the other direction
Buoys can be actuated by the same linkage

## Slide 11: STATIC BALANCING
Potential energy P = f(θ2), θmin < θ2 < θmax
Torque T = -f’(θ2) ~ (P(θ2) - P(θ2 - dθ))/dθ
Mean square torque G = ΣT2/N
Minimize G, subject to:
  Variable bounds for spring parameters as per catalogue & practical considerations
  Spring compression at any point should be within the specified range

## Slide 12: STATIC BALANCING
Case | RMS Value of Input Torque(Nm)
Without balancing | 364.92
With SL06 & SL08 gas spring series | 319.97
With SL10 gas spring series | 14.93
With SL14 gas spring series | 28.60

## Slide 13: STATIC BALANCING

## Slide 14: FORCE ANALYSIS
Quasi-static assumption
Linear mass density : 1 Kg/m
Initial configuration is found & operational range of angle is given as input
Iterate over input angles for force and moment calculations
A*F=B
B= input matrix (accelerations of links)
F= force matrix [ τ Fox Foy F1x F1y F2x F2y F3x F3y]
A= coefficient matrix

## Slide 15: METHOD OF ACTUATION
The driver dyad synthesis is done by optimizing the link lengths for maximum mechanical advantage
The algorithm compares input torque required with the driver dyad output torque
The output of the synthesis is a Grashof-neutral mechanism

## Slide 16: ANIMATION

## Slide 17: THANK YOU
This Project was done under the guidance of Prof. Sujatha Srinivasan as part of the course ME6221: Theory of Mechanisms